## Slide 1
PROJECT PRESENTATION
Edge AI Based Smart EV
Charging Station Optimizer
Nithishkumar S
EGS Pillay Engineering College
e23ecr064@egspec.org

## Slide 2
WHY THIS PROBLEM MATTERS
Introduction
Electric vehicle adoption is growing faster than the charging infrastructure meant to support it. Most charging bays today are passive hardware — they deliver power, but they don't sense, predict, or report anything about how they're being used.
Charging stations rarely expose real-time data on how long a session will last or when the next vehicle is likely to arrive
This makes it hard for an operator to plan bay availability, pre-empt overheating, or simply know the system is healthy without physically checking it
IoT connectivity solves the visibility problem; a small amount of on-device machine learning can go one step further and add prediction, not just monitoring
This project combines both: a connected, sensor-aware charging bay controller with two lightweight AI models running directly on the microcontroller
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
2

## Slide 3
WHAT THE PROJECT SETS OUT TO DO
Objectives
Build a connected EV charging bay controller that senses its own state — power draw, ambient temperature, occupancy — instead of operating blind
Add two on-device machine learning models that predict EV arrival likelihood and expected session duration, without needing a server round-trip
Keep safety independent of the AI: an over-temperature cutoff must work even if a prediction is wrong
Expose all of this on a live cloud dashboard so the system's state is visible remotely, not just at the bay itself
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
3

## Slide 4
WHAT EXISTING RESEARCH SAYS
Literature Survey
IoT in EV charging management
IoT-enabled charging systems consistently report gains in real-time monitoring, predictive maintenance, and energy scheduling over passive hardware [1], [5], [6]
Distributed charging control research treats arrival timing and session length as key variables for any scheduling algorithm to work with — exactly the two things this project's AI models predict [2]
Edge AI / TinyML on microcontrollers
Running inference directly on a microcontroller (rather than a cloud server) is well established as reducing latency and removing a dependency on network availability [3], [4]
Both surveys note that classical ML models (regression, decision trees) are far easier to fit on constrained hardware than deep networks — which shaped the choice of models in this project
Full citations on the References slide at the end of this deck.
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
4

## Slide 5
WHAT THIS PROJECT ACTUALLY DOES
Proposed System
A single EV charging bay is instrumented with sensors for current, voltage, ambient temperature, and humidity, plus two buttons for EV arrival and stop/reset
The controller runs a simple state machine — Available, Charging, Fault — shown on three status LEDs
Every 10 seconds, two on-device AI models estimate the probability of another EV arriving soon and the expected remaining duration of the current session
Every 5 seconds, all sensor readings, state, and both AI predictions are published to a cloud dashboard for remote visibility
An over-temperature safety cutoff is enforced independently of the AI — it doesn't wait for or depend on a model prediction to act
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
5

## Slide 6
HOW DATA MOVES THROUGH THE SYSTEM
System Architecture
Sensors & Buttons
power, temperature, occupancy input
→
Microcontroller Firmware
sensing, safety logic, LEDs
→
Edge AI Inference
arrival + duration models on-device
→
Wireless Link
connects to the cloud broker
→
Cloud Dashboard
live monitoring
The design deliberately separates concerns: sensing and safety logic run locally and don't depend on connectivity; AI inference runs locally too, so predictions keep working even if the network drops; only the reporting layer needs the cloud link.
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
6

## Slide 7
SENSING AND SAFETY LOGIC
Methodology — State Machine & Safety
AVAILABLE
No EV present.
→
CHARGING
EV arrived; session timer running.
→
FAULT
Over-temperature; charging force-stopped.
The over-temperature cutoff is plain firmware logic — it fires regardless of what either AI model predicts, by design
A manual reset path (stop button) always exists, so the system never gets stuck waiting on a network or model response
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
7

## Slide 8
TWO MODELS, TRAINED OFFLINE, RUNNING ON-DEVICE
Methodology — Edge AI Models
Arrival Probability
Logistic Regression
Estimates the chance another EV arrives soon, from time-of-day, occupancy, and recent usage patterns.
Session Duration
Decision Tree Regressor
Estimates how long the current charging session will run, mainly from elapsed time and current draw.
Both models are trained offline on a computer, then converted into plain, dependency-free code that runs on the microcontroller — no cloud call needed for a prediction
Classical models were chosen deliberately over a neural network: they fit comfortably in the memory of a small microcontroller and don't need a hardware accelerator
Honest limitation: training data is currently synthetic, generated to mimic realistic patterns rather than pulled from months of real usage — stated openly, not hidden
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
8

## Slide 9
MAPPING TRAINING TO THIS PROJECT
What I Applied From the Internship
GPIO & sensor interfacing
Every physical input on the bay — the buttons, the LEDs, the temperature/humidity sensor — comes directly from the embedded I/O fundamentals covered early in the internship.
Analog sensing & scaling
Reading raw ADC values and converting them into physically meaningful current/voltage figures follows the same approach taught for interfacing analog sensors.
Wireless connectivity & cloud messaging
The internship's networking module is the reason the bay reports its state remotely at all, instead of being a closed, offline box.
Structuring firmware for a real project
Splitting configuration, sensing, and AI logic into separate files, instead of one long script, reflects the project-organization habits introduced during the training.
Deploying a trained model to constrained hardware
The idea that a model trained in Python doesn't have to stay in Python — that it can be exported and run natively on a microcontroller — came directly from the internship's edge AI material, and is the single most reused concept in this project.
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
9

## Slide 10
WHAT WAS VERIFIED
Results
The bay correctly cycles through Available, Charging, and Fault states in response to real button presses and a simulated temperature rise
The over-temperature cutoff halts charging reliably, independent of whatever the AI models were predicting at that moment
Both AI models produce updated, changing predictions in real time as the underlying sensor and session data changes
All telemetry, including both predictions, reaches the cloud dashboard and updates live
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
10

## Slide 11
Conclusion & Future Scope
Conclusion
The project shows that meaningful prediction — not just monitoring — can run entirely on a small microcontroller, without depending on a cloud service to think
Its scope is intentionally a single-bay decision-support system, not a full multi-bay scheduler
Future Scope
Retrain both models on real logged usage data instead of synthetic data
Extend the approach to multiple bays with an actual scheduling/queueing algorithm
Move from simulated sensors to real current/voltage sensor hardware
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
11

## Slide 12
References
[1] T. Kunj and K. Pal, "Role, application and challenges of IoT in smart EV charging management: a review," Future Batteries, vol. 7, Art. 100102, Elsevier, 2025.
[2] N. I. Nimalsiri, C. P. Mediwaththe, E. L. Ratnam, M. Shaw, D. B. Smith, and S. K. Halgamuge, "A Survey of Algorithms for Distributed Charging Control of Electric Vehicles in Smart Grid," arXiv:1911.06500, 2019.
[3] P. P. Ray, "A review on TinyML: State-of-the-art and prospects," Journal of King Saud University – Computer and Information Sciences, vol. 34, no. 4, 2022.
[4] Y. Abadade et al., "A Comprehensive Survey on TinyML," IEEE Access, vol. 11, 2023.
[5] J. Surendiran et al., "IoT-based advanced electric vehicle charging infrastructure," 2022 Fourth International Conference on Cognitive Computing and Information Processing (CCIP), 2022.
[6] R. J. C. Pinto, J. Pombo, M. R. A. Calado, and S. J. S. Mariano, "An electric vehicle charging station: monitoring and analysis of power quality," 2015 9th International Conference on Compatibility and Power Electronics (CPE), 2015.
Nithishkumar S | EGS Pillay Engineering College | e23ecr064@egspec.org
12