## Slide 1
FINAL PROJECT SUBMISSION
Edge AI Based Smart EV
Charging Station Optimizer
Nithishkumar S
EGS Pillay Engineering College
Internship Provider: Emertxe Information Technologies, Bangalore
Domain: IoT (Embedded IoT Programming) | Cohort: EI26_017 | Duration: 4 Weeks
e23ecr064@egspec.org
github.com/nithishkumars21/Edge_AI_Based_Smart_EV_Charging_Station_Optimizer

## Slide 2
About the Internship
PROGRAM OVERVIEW
Provider | Emertxe Information Technologies, Bangalore
Mode | Online internship
Domain | IoT — Embedded IoT Programming
Duration | 4 weeks
Cohort | EI26_017
Evaluation basis | Regular attendance, quizzes, and on-time project/report submission
Outcome | Completion certificate, issued for college administration purposes
Nithishkumar S | EI26_017 | Emertxe IoT Internship
2

## Slide 3
Project Objective
WHAT THE PROJECT SETS OUT TO DO
Build a single-bay EV charging controller, simulated on an ESP32 in Wokwi, that reports live sensor telemetry to a cloud dashboard and runs two small machine-learning models directly on the microcontroller to support charging decisions.
Integrate analog sensing, digital I/O, and cloud MQTT connectivity in one working firmware stack
Simulate realistic EV bay inputs — voltage, current, ambient temperature and humidity — without physical hardware
Train two Edge AI models offline and deploy them to run inference on-device, with no server round-trip
Add a safety interlock that halts charging independently of the AI models, on over-temperature
Visualize live telemetry and predictions on a ThingsBoard Cloud dashboard
Nithishkumar S | EI26_017 | Emertxe IoT Internship
3

## Slide 4
What I Learned — Build Progression
SKILLS, IN THE ORDER I PICKED THEM UP
01
GPIO fundamentals
Started with basic digital output on the ESP32 — blinking an LED taught me pin modes and the Arduino-style setup()/loop() structure before anything more complex.
02
Analog sensing (ADC)
Learned to read potentiometers as stand-ins for real current/voltage sensors, and to scale raw ADC counts into meaningful physical ranges.
03
Sensor libraries
Interfaced a DHT sensor for temperature and humidity, and learned to double-check a sensor's actual wiring against the code instead of assuming they matched.
04
WiFi + MQTT
Connected the ESP32 to a WiFi network and pushed data to a cloud broker over MQTT — my first real exposure to IoT connectivity end to end.
05
Edge AI deployment
Learned that a model trained in Python with scikit-learn can be exported as plain C code (via m2cgen/micromlgen) and run directly on a microcontroller with no ML runtime needed.
Nithishkumar S | EI26_017 | Emertxe IoT Internship
4

## Slide 5
System Overview
HOW DATA MOVES THROUGH THE SYSTEM
Sensors & Buttons
2x pot, DHT22, 2x pushbutton
→
ESP32 Firmware
sensing, safety logic, LEDs
→
Edge AI Inference
arrival + duration models on-device
→
MQTT Client
PubSubClient over WiFi
→
ThingsBoard Cloud
live dashboard
Sensor and button state is read every loop cycle. Every 10 seconds the two Edge AI models run on the live feature vector; every 5 seconds the full telemetry payload — including AI predictions — is published to ThingsBoard over MQTT.
Nithishkumar S | EI26_017 | Emertxe IoT Internship
5

## Slide 6
Hardware & Wiring (Simulated in Wokwi)
COMPONENTS AND CONNECTIONS
ESP32 Pin | Signal | Connected To
GPIO34 / GPIO35 | Current / Voltage (ADC) | Two potentiometers, simulating live sensors
GPIO15 | DHT22 data | Ambient temperature + humidity sensor
GPIO32 / GPIO33 | Arrival / Stop buttons | Green button = EV plug-in, Red button = stop/reset
GPIO21 / 19 / 18 | Status LEDs | Red = fault, Yellow = charging, Green = available
A DHT11-on-GPIO2 reference in the early training material didn't match the DHT22-on-GPIO15 in the final wiring diagram — the firmware follows the actual circuit above, and that correction is called out explicitly in the written report rather than left unmentioned.
Nithishkumar S | EI26_017 | Emertxe IoT Internship
6

## Slide 7
Edge AI: Two On-Device Models
MACHINE LEARNING THAT RUNS ON THE MICROCONTROLLER
Arrival Probability
Logistic Regression
Estimates the chance another EV arrives soon, from time-of-day, occupancy, and recent usage. Exported to a single linear expression + sigmoid using m2cgen.
Session Duration
Decision Tree Regressor
Estimates how long the current charging session will run, mainly from elapsed time and current draw. Exported as a nested if/else tree using micromlgen.
Shared 6-feature input: hourOfDay, dayOfWeek, bayOccupied, recentAvgCurrent, sessionElapsedMin, historicalArrivalRate
Honest note: both models are trained on a synthetic dataset generated to mimic realistic arrival/duration patterns, not on real logged usage — this is stated as a limitation, not hidden.
Nithishkumar S | EI26_017 | Emertxe IoT Internship
7

## Slide 8
Firmware Logic & Safety Interlock
STATE MACHINE
AVAILABLE
No EV present. Green LED on.
→
CHARGING
Arrival button pressed. Yellow LED on, session timer running.
→
FAULT
Ambient temp ≥ 45°C. Red LED on, charging force-stopped.
The over-temperature cutoff is enforced in plain firmware logic, independent of the AI models — safety doesn't depend on the ML predictions being right
The stop button both ends a session and clears a fault, giving a manual reset path at all times
Nithishkumar S | EI26_017 | Emertxe IoT Internship
8

## Slide 9
ThingsBoard Cloud Dashboard
LIVE TELEMETRY & AI OUTPUT
Device connects over MQTT and publishes a JSON telemetry payload every 5 seconds
Payload includes raw sensor readings (voltage, current, power, temperature, humidity) alongside bay state (occupied, fault) and both AI predictions (arrival probability, predicted duration)
Dashboard widgets: time-series chart for voltage/current/power, a gauge for ambient temperature, value cards for occupancy/fault/session data, and a gauge for arrival probability
[ Dashboard screenshot inserted here before submission ]
Nithishkumar S | EI26_017 | Emertxe IoT Internship
9

## Slide 10
Testing & Results
WHAT WAS VERIFIED, AND HOW
# | Test performed | Result
1 | Power on, idle | Green LED on; dashboard shows bay unoccupied
2 | Press arrival button | Yellow LED on; session timer starts climbing
3 | Raise DHT22 temperature above 45°C | Red LED on; charging force-stopped; fault flag set
4 | Press stop button | Fault clears; system returns to available
5 | Watch dashboard for 60+ seconds | All telemetry fields and AI predictions update live
Nithishkumar S | EI26_017 | Emertxe IoT Internship
10

## Slide 11
Challenges I Ran Into (and Fixed)
REAL DEBUGGING, NOT JUST THE HAPPY PATH
WiFi never connected
An empty-string WiFi password was silently mishandled on an open network. Switching to the single-argument WiFi.begin() call fixed it.
MQTT rejected the token (rc=5)
Turned out to be a regional mismatch — my ThingsBoard account was on the EU Cloud instance, but the firmware pointed at the default (US) broker address.
Build failed after a manual edit
A missing closing brace in setup() cascaded into five unrelated-looking compiler errors. Learned to check brace-matching first when errors look scattered.
Dashboard widgets showed "N/A"
Default demo widgets were bound to placeholder key names that didn't match my actual telemetry keys — had to rebind each widget to the real key.
Nithishkumar S | EI26_017 | Emertxe IoT Internship
11

## Slide 12
Skills Gained From This Internship
TECHNICAL AND PRACTICAL
Technical
Embedded C++ on ESP32 (Arduino framework)
IoT protocols: MQTT, WiFi provisioning, NTP time sync
Cloud IoT dashboards (ThingsBoard): devices, telemetry, widgets
Deploying trained ML models to a microcontroller (m2cgen, micromlgen)
Circuit simulation and wiring in Wokwi
Practical / Process
Reading compiler errors and terminal logs systematically instead of guessing
Isolating a bug to one layer (network vs. code vs. cloud config) before changing anything
Documenting a project honestly, including its limitations
Working through a multi-day build in stages rather than all at once
Nithishkumar S | EI26_017 | Emertxe IoT Internship
12

## Slide 13
Limitations & Future Scope
STATED HONESTLY, NOT HIDDEN
Current Limitations
ML models trained on synthetic, not real, usage data
Voltage/current are potentiometer proxies, not real sensors
Single bay only — no multi-bay scheduling yet
No battery-backed RTC; time comes from NTP after WiFi connects
Future Scope
Retrain models on real ThingsBoard-logged usage data
Extend to multiple bays with an actual queueing/scheduling algorithm
Replace potentiometers with real current/voltage sensor ICs on physical hardware
Add MQTT over TLS and per-device provisioning
Nithishkumar S | EI26_017 | Emertxe IoT Internship
13

## Slide 14
Conclusion
This internship took me from single-pin GPIO control to a working, cloud-connected system running machine learning inference on a microcontroller — built by integrating each week's individual lesson into one functioning project, debugged the way real embedded projects actually get debugged.
Thank you
Nithishkumar S | e23ecr064@egspec.org | EGS Pillay Engineering College | Emertxe IoT Internship, Cohort EI26_017
github.com/nithishkumars21/Edge_AI_Based_Smart_EV_Charging_Station_Optimizer